## Slide 1
Xiaoyu Jin1, Kamal Chowdhury2, Thanh Duc Dang3, Ranjit Deshmukh4, Stefano Galelli5
  1. Background
Will history repeat itself? A quantitative analysis of Myanmar’s
future energy pathways and their impact on free-flowing rivers
1 Dalian University of Technology; 2 University of Maryland; 3 University of South Florida; 4 University of California Santa Barbara; 5 Cornell University
Several river basins in Southeast Asia have recently witnessed the construction of new hydropower dams. This is the result of energy policies hinged on the exploitation of cheap and locally-available energy resources.
(a) River basins supporting Myanmar’s power grid. Existing and planned dams are denoted in blue and red, respectively. (b) Graphical representation of Myanmar’s power generation and transmission fleet operated in 2020.
  2. Research questions
What are the key drivers of future hydropower development in the Irrawaddy and Salween rivers?
Could decarbonization policies further push hydropower development?
Is there any potential conflict between water and other natural resources (e.g., land)?
  3. Modelling framework
  4. Experimental setup
CAPACITY EXPANSION MODEL
HYDROLOGICAL MODEL
  REZoning + Renewables.ninja
RENEWABLE ENERGY POTENTIAL MODEL
  Power generation fleet, costs, emissions
  Meteorological forcings
  Solar and wind availability
  Hydropower availability
  Electricity demand
  Climate policies
  VIC-Res
We hypothesize that future hydropower development (over the period 2020-2050) could be influenced by three main drivers, namely future hydrological conditions, electricity demand, and decarbonization policies.
GC33K-1284
Contact us
For the hydrological conditions, we consider four scenarios, one representing ‘Historical’ conditions and three representing ‘Minimum’, ‘Maximum’, and ‘Median’ future conditions. The latter are derived from an an ensemble of 10 global climate models and three carbon emission scenarios.
Four decarbonization policies based on:
  Imposing no decarbonization targets
  Limiting the 2050 emissions to the 2020 level
  Reducing annual emissions to 50% of the 2020 level (in 2050)
  Reaching carbon neutrality in 2050
Future electricity demand is modelled with four scenarios, illustrated in the figure below.
  5. Results
  x
Annual load projections. The ‘Reference’ scenario is based on technical reports, while the scenarios corresponding to SSP 1, 2, and 3 are produced by an integrated assessment model (GCAM).
The Irrawaddy and Salween rivers, however, represent an exception: their vast hydropower potential (about 100 GW) has, so far, seen limited hydropower development, making them the main free-flowing rivers of Southeast Asia.
Characterizing the conditions under which Myanmar could expand its grid without damaging these rivers is therefore necessary to avoid repeating past mistakes, like the ones characterizing the nearby Mekong River basin.
Key takeaways:
The impact of electricity demand on the LHD is substantial, but the demand-LHD relationship is non-linear.
The decarbonization policy does not strongly affect hydropower development.
Both points are due to the concomitant expansion of other generation sources (e.g., solar, gas).
Drier conditions reduce the dam capacity factor, in turn requiring the construction of more dams.
We have a total of 64 scenarios, or states of the world, w.r.t. which we study the expansion of Myanmar’s power system, including its future hydropower fleet. The figure below illustrates the Level of Hydropower Development (LHD) at the end of the planning period.
Level of hydropower development in 2050, defined as the ratio between constructed and planned dams. The circles illustrated in the rightmost panel correspond to specific scenarios that are further analyzed in the plot below.
Electricity generation mix across the period 2020-2050 for four selected scenarios.
Code
  GridPath
VIC-Res: https://github.com/Critical-Infrastructure-Systems-Lab/VICRes
Web: https://galelli.cee.cornell.edu
Email: galelli@cornell.edu
REZoning: https://rezoning.energydata.info
GridPath: https://www.gridpath.io
Renewables.ninja: https://www.renewables.ninja