## Slide 1
Evaluating Streamflow Forecasts in Hydro-Dominated Power Systems:
When and Why They Matter
Rachel Koh1,2
Stefano Galelli2,3
May 21, 2024
1Centre for Climate Research Singapore
2Singapore University of Technology and Design
3Cornell University
CIS
Lab

## Slide 2
Value of streamflow forecasts
  Common metrics
  Flood control
  Irrigation supply
  Spilled water
  Hydropower ‘production’
  Typically based on the output of a water system model

## Slide 3
Value of streamflow forecasts
  Common metrics
  Flood control
  Irrigation supply
  Spilled water
  Overlooks the role played by dams and forecasts in the power system
  Hydropower ‘production’
Notes: In particular, it is important to understand which aspects of power system operations are improved by the use of streamflow forecasts, when forecasts are most useful, and how forecast predictive performance translates into different metrics of system performance. All these aspects would indeed be relevant to support the operationalization of streamflow forecasts.

## Slide 4
Research questions
  How does forecast value change as we consider different performance aspects of a power grid? When is the use of forecasts more beneficial?
  How does forecast predictive performance affect power system operations?
  Is forecast value affected by the interdependencies of the water-energy system?

## Slide 5
Case study
  Cambodian power system
  6 hydropower dams (1,048 MW)
  18 thermoelectric units (682 MW)
  Import from Thailand, Laos, and Vietnam
  Peak demand of 1,068 MW

## Slide 6
Data
  Inflow to hydropower reservoirs
  Retrieved from the Global Flood Awareness System (GloFAS) database
    From 1979 to near real‐time with daily resolution
  Inflow forecasts
  Retrieved from GloFAS
    Available for 2 days weekly (every Monday and Thursday)
    24‐hr time step and up to 46‐day lead time
    From January 1999 to December 2018
  Common period 2000-2018
Notes: Add a figure from a GloFAS paper / website

## Slide 7
Models
Water system model
Inflow /
Inflow forecasts
Dispatchable hydropower
Streamflow routing module (with dam operations)
Reservoir storage, release, dispatchable hydropower
Generation technology
Target storage levels

## Slide 8
Models
Water system model
Inflow /
Inflow forecasts
Dispatchable hydropower
Streamflow routing module (with dam operations)
Generation mix
+
Costs, CO2 emissions, N-1 violations
Techno-economic parameters of thermoelectric units
Transmission capacity
PowNet
(MILP problem: minimize production cost, meet demand)
Dispatchable wind
and solar
Reservoir storage, release, dispatchable hydropower
Hourly electricity demand
Generation technology
Other parameters
Chowdhury et al. (2020), Journal of Open Research Software, 8(1).
Target storage levels

## Slide 9
Models
Water system model
Inflow /
Inflow forecasts
Dispatchable hydropower
Streamflow routing module (with dam operations)
Generation mix
+
Costs, CO2 emissions, N-1 violations
Techno-economic parameters of thermoelectric units
Transmission capacity
PowNet
(MILP problem: minimize production cost, meet demand)
Dispatchable wind
and solar
Reservoir storage, release, dispatchable hydropower
Hourly electricity demand
Generation technology
Other parameters
Chowdhury et al. (2020), Journal of Open Research Software, 8(1).
Target storage levels
Dispatched hydropower

## Slide 10
Experimental setup
  Reservoir operating schemes
  Static rule curves (no forecasts)
  Model Predictive Control (forecast-informed)
    Perfect forecasts
    Climatology
    Ensemble mean

## Slide 11
Experimental setup
  Forecast predictive performance
  Symmetric Mean Absolute Percentage Error (SMAPE)
  Forecast value
  Dispatchable hydropower
  Dispatched and unused hydropower
  System operating costs
  CO2 emissions
  Number of N‐1 violations
Water system model
PowNet

## Slide 12
Results
  Value of streamflow forecasts
Not all available hydropower is dispatched by the grid
Defining value in terms of different metrics leads to different conclusions
The benefits of operating with forecasts are accentuated during the post-monsoon season

## Slide 13
Results
  Value of streamflow forecasts

## Slide 14
Results
  Intra‐ and Inter‐Annual Variability of Forecast Value
Difference between hydropower dispatched by forecast-informed schemes and rule curves

## Slide 15
Results
  Relationship Between Forecast Predictive Performance and Value
The correlation between forecast error and performance metrics decreases as we ‘move’ from the water to the power system.

## Slide 16
Results
  Relationship Between Forecast Predictive Performance and Value

## Slide 17
Results
  Effect of re-operation

## Slide 18
Conclusions
  Defining forecast value in terms of different performance metrics produces different outcomes
  Measuring value in terms of available hydropower gives us a narrow view of forecast value
  Streamflow forecasts are useful (in terms of costs, CO2 emissions etc.) but such value changes throughout the year
  A tighter integration of water and power system operations enhances the role of electricity demand and dwarfs the role forecasts

## Slide 19
Thank you!
galelli@cornell.edu
https://galelli.cee.cornell.edu
@GalelliStefano

## Slide 20
Forecast predictive performance

## Slide 21
Design specifications of dams

## Slide 22
Rule curves
  Example

## Slide 23
Choice of the MPC horizon

## Slide 24
Generation mix

## Slide 25
Results
  Intra‐ and Inter‐Annual Variability of Forecast Value
Hydrological conditions that are favorable to forecast-informed schemes

## Slide 26
Value of streamflow forecasts