## Slide 1
Balancing Accuracy and Computing Costs: Are Decomposition Methods Still Needed in the Era of Optimization Frameworks?
October 17
2023 INFORMS Annual Meeting
P. Bunnak1, S. Coniglio2, S. Galelli1
1 Cornell University
2 University of Bergamo
CIS
Lab

## Slide 2
Energy / power system analysis
Common challenges
Representation of interactions with other socio-economic sectors
Analyses across large(r) spatio-temporal domains
Integration of weather and climate uncertainty
Increase in computational requirements

## Slide 3
Increase in computational requirements
Example
Koh et al. (2022), Applied Energy, 321, 119386
  Cambodian power system
  Installed capacity ~ 2 GW
  Hydropower capacity ~ 1 GW

## Slide 4
Increase in computational requirements
Example
  1000-year synthetic dataset of daily streamflow, solar irradiance and load
Koh et al. (2022), Applied Energy, 321, 119386
Notes: - Kirsch–Nowak Streamflow Generator

## Slide 5
Increase in computational requirements
Example
  System’s response (evaluated via simulation)
Koh et al. (2022), Applied Energy, 321, 119386
  Run time ~ 7,900 sec
Notes: - 0.0215 s

## Slide 6
Balancing Accuracy and Computing Costs
  Rely on faster optimization frameworks
Strategies
  Algebraic (opt.) modeling languages
  Solver
Better connection between data analysis packages (e.g., xarray and pandas) with solvers
  Time-to-build
  Time-to-solve

## Slide 7
Balancing Accuracy and Computing Costs
  Rely on faster optimization frameworks
  Adopt simplifications of temporal, spatial, or technological dimensions
Strategies
  Reduce the number of weather events
  Aggregate the representation of power fleet components into macro areas
  Smaller uncertainty set
  Less decision variables
  Generator
  Sub-station

## Slide 8
Balancing Accuracy and Computing Costs
  Rely on faster optimization frameworks
  Adopt simplifications of temporal, spatial, or technological dimensions
Strategies
  Reduce the number of weather events
  Aggregate the representation of power fleet components into macro areas
  Less decision variables
  Generator
  Sub-station
  Smaller uncertainty set

## Slide 9
Balancing Accuracy and Computing Costs
  Rely on faster optimization frameworks
  Adopt simplifications of temporal, spatial, or technological dimensions
Strategies
  Reduce the number of weather events
  Aggregate the representation of power fleet components into macro areas
  Drop the representation of unit commitment
  Less decision variables
  Simpler formulation (MILP  LP, MINLP  NLP)
  Smaller uncertainty set
 structural uncertainty

## Slide 10
Balancing Accuracy and Computing Costs
  Rely on faster optimization frameworks
  Adopt simplifications of temporal, spatial, or technological dimensions
  Build on decomposition methods
Strategies
  Computing costs
  (time-to-solve)
  Accuracy

## Slide 11
Decomposition methods
  Structural forms of large-scale problems
  Variable
  Constraint
Source: Bradley et al. (1977), Applied Mathematical Programming.
  Nearly independent subsystems
  Coupling constraints
  Coupling variables
  Visualization of the A matrix

## Slide 12
Decomposition methods
  Structural forms of large-scale problems
  Variable
  Constraint
Source: Bradley et al. (1977), Applied Mathematical Programming.
  Coupling constraints
  Subproblems
  Visualization of the A matrix
Notes: - Decomposition vs column generation?

## Slide 13
Decomposition methods
  Advantages
  Preserve the original problem formulation / delay decisions on its simplification
  Reduce computing costs
  Allow for parallel computation
  Computing costs
  (time-to-build)
  Accuracy

## Slide 14
PowNet
Dispatchable hydropower
Generation mix, power flow
+
Costs, CO2 emissions
Techno-economic parameters of thermoelectric units
Transmission capacity
PowNet
(MILP problem: minimize production cost, meet demand)
Dispatchable wind
and solar
Hourly electricity demand
Generation technology
Other parameters
Chowdhury et al. (2020), Journal of Open Research Software, 8(1)
https://github.com/Critical-Infrastructure-Systems-Lab

## Slide 15
PowNet + Dantzig-Wolfe decomposition
  Master problem
  Flow balance
  Reserve requirement
  Renewable/Import bound
  Transmission
    Min/Max line capacity
    Voltage angle
    Reference node
  ‘Self-scheduling’ sub-problems
  Minimum-down
  Minimum-up time
  Ramp down
  Ramp up
  MIP tightening constraints
    Strengthened minimum-down time
    Strengthened minimum-up time
    Trajectory down
    Trajectory up
    Relationship between variables
    Dispatch linkage
    Status linkage

## Slide 16
PowNet + Dantzig-Wolfe decomposition
  Example – ‘dummy’ power system
Node1
MaxDemand
700 MW
pGas
lineCap
1762 MW
Node 3
lineCap
1762 MW
node2
MaxDemand
102 MW
lineCap
80 MW
pHydro
Max = 36 MW
lineCap
100 MW
pOil
pBiomass
lineCap
200 MW
lineCap
300 MW
Buyer
MaxDemand
32 MW
Supplier
Max 60 MW
lineCap
80 MW
lineCap
300 MW
  Visualization of the A matrix

## Slide 17
Experimental setup
  Formulation based on Knueven et al. (2020)
  Implementation in Gurobipy + Gurobi
  PowNet 2.0 vs PowNet 2.0 + DW
  Experiments carried out on Hopper Cluster (@Cornell CAC)
    Dual 20-core Intel Xeon Gold 5218R CPUs @ 2.1 GHz, 192 GB of RAM
    OpenHPC 2.3 with Rocky Linux 8.4
    Gurobi 9.5.1
  Modeling instances (24 hours)
    ‘Dummy’ power system (1,411 constraints and 1,056 variables)
    Cambodia (8,364 constraints and 5,952 variables)
    Thailand (74,633 constraints and 54,312 variables)
Knueven et al. (2020), INFORMS Journal on Computing, 32(4)
  PowNet 2.0

## Slide 18
Preliminary results
  ‘Dummy’ power system (3 Blocks)
Node1
MaxDemand
700 MW
pGas
lineCap
1762 MW
Node 3
lineCap
1762 MW
node2
MaxDemand
102 MW
lineCap
80 MW
pHydro
Max = 36 MW
lineCap
100 MW
pOil
pBiomass
lineCap
200 MW
lineCap
300 MW
Buyer
MaxDemand
32 MW
Supplier
Max 60 MW
lineCap
80 MW
lineCap
300 MW
 | PowNet | PowNet+DW
Obj. f. | 1,612,145 | 1,629,253
Time-to-solve, TOT (sec) | 0.0084 | 0.4692
Time-to-solve, Master problem (sec) | - | 0.0976
Time-to-solve, Sub-problems (sec) | - | 0.3716

## Slide 19
Preliminary results
  ‘Dummy’ power system (3 Blocks)
 | PowNet | PowNet+DW
Obj. f. | 1,612,145 | 1,629,253
Time-to-solve, TOT (sec) | 0.0084 | 0.4692
Time-to-solve, Master problem (sec) | - | 0.0976
Time-to-solve, Sub-problems (sec) | - | 0.3716
  Optimality gap:
  1.06%
  Visualization of the A matrix

## Slide 20
Preliminary results
  ‘Dummy’ power system (3 Blocks)
 | PowNet | PowNet+DW
Obj. f. | 1,612,145 | 1,629,253
Time-to-solve, TOT (sec) | 0.0084 | 0.4692
Time-to-solve, Master problem (sec) | - | 0.0976
Time-to-solve, Sub-problems (sec) | - | 0.3716
  Optimality gap:
  1.06%

## Slide 21
Preliminary results
  Cambodia’s grid (18 Blocks)
 | PowNet | PowNet+DW
Obj. f. | 438,281 | 451,075
Time-to-solve, TOT (sec) | 0.0215 | 0.6643
Time-to-solve, Master problem (sec) | - | 0.0943
Time-to-solve, Sub-problems (sec) | - | 0.5700

## Slide 22
Preliminary results
  Cambodia’s grid (18 Blocks)
  Optimality gap:
  % 2.92
  Visualization of the A matrix
 | PowNet | PowNet+DW
Obj. f. | 438,281 | 451,075
Time-to-solve, TOT (sec) | 0.0215 | 0.6643
Time-to-solve, Master problem (sec) | - | 0.0943
Time-to-solve, Sub-problems (sec) | - | 0.5700

## Slide 23
Preliminary results
  Thai grid (151 Blocks)
 | PowNet | PowNet+DW
Obj. f. | 36,888,014 | 38,763,317
Time-to-solve, TOT (sec) | 13.3008 | 19.8815
Time-to-solve, Master problem (sec) | - | 12.1936
Time-to-solve, Sub-problems (sec) | - | 7.6879

## Slide 24
Preliminary results
  Thai grid (151 Blocks)
  Optimality gap:
  % 5.08
  Visualization of the A matrix
 | PowNet | PowNet+DW
Obj. f. | 36,888,014 | 38,763,317
Time-to-solve, TOT (sec) | 13.3008 | 19.8815
Time-to-solve, Master problem (sec) | - | 12.1936
Time-to-solve, Sub-problems (sec) | - | 7.6879
  Potential for parallelization

## Slide 25
Conclusions
  Implementation of DW decomposition for a large-scale power system model
  # decision variables
  Computing costs
  PowNet
  PowNet + DW

## Slide 26
Conclusions
  Implementation of DW decomposition for a large-scale power system model
  Major improvements expected with
    Parallelization schemes
  # decision variables
  Computing costs
  PowNet
  PowNet + DW
  PowNet + DW + Parallel.

## Slide 27
Conclusions
  Implementation of DW decomposition for a large-scale power system model
  Major improvements expected with
    Parallelization schemes
    Larger grids
  ASEAN Power Grid

## Slide 28
Conclusions
  Implementation of DW decomposition for a large-scale power system model
  Major improvements expected with
    Parallelization schemes
    Larger grids
  PowNet 2.0 + DW implementation to be released on GitHub PowNet’s webpage
  ASEAN Power Grid

## Slide 29
Acknowledgments
  Phumthep Bunnak
  Stefano Coniglio

## Slide 30
Thank you!
galelli@cornell.edu
https://galelli.cee.cornell.edu
@GalelliStefano
CIS
Lab